## Slide 1: Minnesota Elevation Mapping Project
Metro Area Collect
1/13/2011
Tim Loesch
Minnesota Department of Natural Resources

## Slide 2: Metro Area LiDAR Project
Agenda
  Welcome and Introductions
  Overview of Minnesota Elevation Mapping Project
    LiDAR Specifications
    Project Deliverables
  Costs and Collection Buy-Up Options
  Partnerships
    Survey Test Shots
    GIS Contacts

## Slide 3: Metro Area LiDAR Project
Clean Water Legacy Funds
  $5,600,000 funding
  Project Phases
    MN River Basin
      Funded and acquisition complete
    Arrowhead Region
      Funded – Spring 2011
    Metro Region
      Funded – Spring 2011
    Central Lakes Region
      Unfunded – Spring 2012

## Slide 4: Metro Area LiDAR Project
State Specifications
  Modeled after USGS Base LiDAR Spec V13
    Vertical Accuracy 15 cm
    Horizontal Accuracy < 1m
    Projection - UTM Zone 15
    Horizontal Datum - NAD83
    Vertical Datum – NAVD88
    Nominal Pulse Spacing 1.5 meters

## Slide 5: Metro Area LiDAR Project
Data Deliverables
  Classified LiDAR Points – LAS format
    Bare Earth
    Bridges
    Buildings
    Vegetation
    Water

## Slide 6: Metro Area LiDAR Project
Digital Elevation Models
  One Meter
  Three Meter
  Hillshade
  Hydro Flattened using Edge of Water Breaklines

## Slide 7: Metro Area LiDAR Project
Data Deliverables
  Edge of Water Breaklines
    Lakes and Ponds > 2 acres
    Rivers and Streams > 100’ wide
    Used for:
      Hydro Flattening
      Contour Enforcement

## Slide 8: Metro Area LiDAR Project
Data Deliverables
  2’ Contours
  Building outlines

## Slide 9: Metro Area LiDAR Project
Data will be provided to county partners
  External Hard Drive that you keep
    LiDAR points (LAS Files)
    DEMs – 1 and 3 meter
    Hillshades
    2’ contours
    Building outlines
  All products delivered in ESRI Geodatabase format

## Slide 10: Metro Area LiDAR Project
Project Costs
  Eleven Counties
    Anoka, Carver, Dakota, Goodhue, Hennepin, Isanti, Meeker, Ramsey, Scott, Sherburne, Washington
  5,667 Square Miles
Pulse Spacing | Cost/sq mile | Total Cost
1.5 | $133.12 | $754,391

## Slide 11: Metro Area LiDAR Project
Buy up Options
  The selected vendor has quoted some buy-up costs for increased point density
  Costs listed below are examples but vendor claims they can produce anything up to 12 pts/meter
Pulse Spacing | Cost/sq mile | Minimum Area | Total Est. Cost
2pts/meter2 | $190.12 | 1000 square miles | $190,000
5pts/meter2 | $419.00 | 1000 square miles | $490,000
12pts/meter2 | $861.00 | 1000 square miles | $891,000

## Slide 12: Metro Area LiDAR Project
Buy-up costs are the responsibility of the counties interested
County will need to work with vendor:
  Specifications
  Contracting
  Invoicing
DNR will still receive data and do QA/QC

## Slide 13: Metro Area LiDAR Project
Partnership Opportunities
  Validation Points
    To help ensure that we get what we pay for
  GIS Points of Contact
    To server internal county customer needs

## Slide 14: Validation Points
Winona County Validation Points

## Slide 15: Validation Points
371.93
LiDAR points
Interpolated Value
372.115

## Slide 16: Validation Points
--------- Report Summary ---------
Error Mean: -0.116
Error Range: [-0.435,0.143]
Skew: -0.305
RMSE(z): 0.161
NMAS/VMAS
Accuracy(z) (90% CI): ±0.265
ASPRS/NSSDA
Accuracy(z) (95% CI): ±0.315
176 control points included in summary out of 176
- 0 control points turned off
- 0 control points returned no-data
--------- Control Points ---------
Name Control X Control Y Control Z Surface Z Error
L1O0 604760.340 4878787.629 201.217 201.389 -0.172
L5U1 608921.294 4878065.350 201.488 201.806 -0.318
L1O2 610991.353 4876621.369 200.214 200.397 -0.183
L1O3 607292.402 4874401.804 233.428 233.606 -0.178
L1O4 622397.772 4873262.387 207.292 207.356 -0.064
L1O5 626922.206 4869248.810 202.936 202.969 -0.033
L1O6 631669.497 4863815.331 200.254 200.333 -0.079
L1O7 635439.901 4857649.190 375.011 375.070 -0.059
L1O8 625518.897 4864620.423 385.756 385.722 0.034
L2T9 621174.012 4864494.226 388.359 388.470 -0.111
L2T10 620283.975 4857065.579 386.810 387.048 -0.238

## Slide 17: Validation Points
Winona County Validation Report
RMSE across cover Types
Chart: 
| RMSE
L1O | 0.12702
L2T | 0.16646
L3B | 0.19557
L4F | 0.17223
L5U | 0.13616
Overall | 0.16082